     How An Acousto-Optic Modulator Works
By Matt D'Addario
April 3, 2014
PHYS 4P62

---
What is an Acousto-Optic Modulator (AOM)?
- An AOM is a device that uses the acousto-optic effect to shift the frequency, intensity or direction of light by using sound waves.
- An AOM consists of a transducer (usually a piezo-electric transducer or PZT), a transparent medium (glass such as crystalline quartz for example) and an electrical drive signal that produces a radio frequency.
- AOM's are used in the field of telecommunications for signal modulation, spectroscopy for frequency control and other various optical applications.

---
What is the acousto-optic effect?
- The acousto-optic effect is an example of photoelasticity.
- Photoelasticity is a type of property in some transparent materials, such as glass, while under stress. When photoelastic materials are subjected to pressure, internal strains develop that can be observed.
- An internal strain is caused by acoustic waves propagating through the material and this strain causes a change in the material's refractive index, by altering the density as the sound waves pass through the material.

---
What is the acousto-optic effect?
- This change in refractive index of the material due to the acoustic waves is also changes with respect to position in the material, since the acoustic waves are moving.
- The following expression describes the change in refractive index caused by the sound waves, travelling along the z-axis:
- Where
- Is the photoelastic tensor.
- This new refractive index acts as a diffraction grating travelling through the material and therefore will diffract any light that is incident on the material. This is why it is called the acousto-optic effect, since it is in interaction of sound and light.

---
How does an Acousto-Optic Modulator work?
- An AOM works by attaching a transducer to a material (glass), which electric signals are sent through and cause the piezo-electric transducer (PZT) to convert the electric signals into mechanical vibrations and thus into acoustic sound waves throughout the material.
- These sound waves then change the refractive index of the material due to the acousto-optic effect that was discussed earlier.
- These sound waves can be treated as crests of increased refractive index and alternate with troughs of decreased refractive index. The changing refractive index creates a gradient, which the light beam is interacting with and this interaction is called Brillouin scattering.

---
Brillouin Scattering
- Let's take a closer look at how the light beam is diffracted by the sound waves.
- Brillouin scattering occurs when there is an interaction between light and acoustic modes or phonons. This interaction brings about an inelastic scattering of photons with the sound waves propagating through the material.
- The following expression shows the relationship between the wavelength of the sound waves, , the wavelength of the incident light beam and the scattering angle, .

---
How does an Acousto-Optic Modulator work?
- When the light is scattered from successive wavefronts, constructive interference is formed. The condition for constructive interference is the following:
- Where n is an integer, θi is angle of incidence and θd is the angle of diffraction.
- Once the light beam is scattered due to the interaction with the sound waves (Brillouin scattering), it then exits the AOM.
- The exited light beam from the AOM can be manipulated and changed in various ways. There are four properties of the exit beam that can be controlled, the deflection, intensity, frequency and phase of the exit light beam can all be modulated and controlled in the following techniques.

---
Deflection
- The first property of the exit light beam that can be controlled is the deflection of the beam. This can be accomplished by changing the wavelength of the incident light beam. The following equation shows this;
- Where θ is the angle at which the beam exits the AOM, λ is the wavelength of the incident light beam and is the wavelength of the sound wave.

---
Intensity
- The intensity of the exit laser beam can also be modified by increasing the intensity of the sound wave. This is done by changing the drive signal to the PZT, which increases the amplitude of the acoustic wave and therefore its intensity.
- This type of adjustment is called amplitude-modulating (AM) and is the best way to control the intensity of the exit light beam because it allows us to precisely control the intensity of the exit light beam.

---
Frequency
- The frequency of the exit laser beam can also be controlled because the light is scattering off of moving phonons, since the sound waves are propagating through the material.
- The frequency of the exit beam will then be doppler shifted by an amount of , where is the frequency of the sound wave, therefore
- So we see that the frequency of the exit laser beam can be controlled by changing the frequency of the signal to the PZT because this will change the frequency of the acoustic sound wave.
- This method is called frequency-modulating (FM).

---
Phase Shift
- The phase shift of the exit light beams may also be controlled because the acoustic sound waves add a phase shift to the diffracted light beam.
- This phase can be controlled and changed by any amount by changing the phase of the signal, which will then change the phase of the sound waves and create a different phase shift for the exit light beam.

---
Applications of AOMs
- One application for an AOM is in laser printers, where it is used for modulating the power of a laser beam. The AOM is there to control the power or intensity of the laser beam in a laser printer.
- AOMs are also used to shift the frequencies of laser beams for various measurement schemes.
- AOMs are also used in something called mode-locking, which is a technique in which a laser is made to produce pulses of light of very short durations such as on the order of picoseconds and femtoseconds.